# EPIMETHEUS FPGA/CPLD Specification

This document describes the Verilog code which is the core of the Epimetheus (EPI) CPLD functionality. The board block diagram is shown below:

EPIMETHEUS Block Diagram

# Functional Description
The main mission of the Epi CPLD is to provide programmed Outputs for the various facilities on EPI and to be capable of sending a message to the host processor on Ozy whenever a state change occurs on the 'receive_in” pins (like a button push).
The I2C bus is used both as the programming path AND the message path. There are two I2C ports on the device primarily to simplify internal tristate control. These should be tied together on a single I2C bus on the EPI board.
The Verilog code for Epimetheus implements an I2C slave which translates I2C activity into Wishbone bus cycles. These Wishbone transactions can target one of three slaves, the I2C Master (from OpenCores), the “Epi_ctl_regs” module, and the “Status_mcode” module. The “Status_ctl” module serves as another Wishbone master which causes messages over the I2C master every time a signal changes state on the “receive_in” lines. The “Wb_arb_mux” module serves as an arbiter between the two Wishbone bus masters and feeds the data bus to/from each of the three I2C slaves.
A block Diagram of the EPIMETHEUS code is illustrated below:

HPSDR
I2C Slave
Deglitch
Deglitch
OpenCores
I2C Master
Deglitch
Deglitch

Status
mcode
Status
Ctl
Wb Arb
Mux

Epi Ctl Regs

Wishbone

receive_in
cross_point
relay_out
oc_out
slv_sda
slv_scl
mstr_sda
mstr_scl

Epi Verilog Code Block Diagram

This document covers all of the modules colored in Blue. The “OpenCores I2C Master” has it's own documentation that can be found on the “www.opencores.org” web page.

## EPI Module description

This module is the top level and incorporates several sub-modules which implement the CPLD functionality. The table below illustrates the module I/Os.

Signal Name	Width	Direction	Description
reset_n	1	In	Reset (Active low)
CLK	1	In	Clock input – should be 30-40Mhz
slv_sda	1	In/Out	I2C Slave Serial Data
slv_scl	1	In	I2C Slave Serial Clock
mstr_sda	1	In/Out	I2CMaster Serial Data
mstr_scl	1	In/Out	I2C Master Serial Clock
cross_point_ctl	48	Out	Cross Point Control
relay_out	8	Out	Relay Control
receive_in	8	In	Received Inputs
oc_out	8	Out	Open Collector Out

## OpenCores I2C Master
The OpenCores I2C master is a wishbone slave that is employed within this design to send messages to the system host (Ozy) when any bit within “receive_in” changes state. The initial conditions are set up by the I2C slave from Ozy, then the microcode inside “Status_mcode” that drives “Status_ctl” will send a copy of the “receive_in” bus anytime a bit changes state.
The table below illustrates the module I/O – please see the OpenCores I2C Master document for further design details.

Signal Name	Width	Direction	Description
wb_clk_i	1	In	Wishbone Clock
wb_rst_i	1	In	Wishbone Reset
arst_i	1	In	Asynchronouse reset
wb_adr_i	3	In	Wishbone Address
wb_dat_i	8	In	Wishbone Data In
wb_dat_o	8	Out	Wishbone Data Out
wb_we_i	1	In	Wishbone Write
wb_stb_i	1	In	Wishbone Strobe/Select
wb_cyc_i	1	In	Wishbone Cycle
wb_ack_o	1	Out	Wishbone Ack
wb_inta_o	1	Out	Wishbone Interrupt Out
scl_pad_i	1	In	I2C Clock In
scl_pad_o	1	Out	I2C Clock Out
scl_padoen_o	1	Out	I2C Clock Pad Out Enable (active low)
sda_pad_i	1	In	I2C Data In
sda_pad_o	1	Out	I2C Data Out
sda_padoen_o	1	Out	I2C Data Pad Out Enable (active low)

Please see the register description section for register bit definitions.

The define ADDRESS sets the I2C Slave address.

## I2C_SLAVE (HPSDR)
This module implements an I2C slave which translates I2C transactions into Wishbone operations.
The module receives it's I2C address from the top level module (the address which it responds on the I2C too). It is assumed that the I2C signals are de-glitched and that SDA occurs AFTER SCL to allow the STOP & START states to be determined reliably.

Signal Name	Width	Direction	Description
rst_n	1	In	Clock
clk	1	In	reset (active low)
my_addr	7	In	I2C Slave Address
adr_o	8	Out	Wishbone Address
dat_i	8	In	Wishbone Data In
dat_o	8	Out	Wishbone Data Out
we_o	1	Out	Wishbone Write
stb_o	1	Out	Wishbone Strobe
sel_o	1	Out	Wishbone Select (redundant with strobe)
cyc_o	1	Out	Wishbone Cycle
ack_i	1	In	Wishbone Ack
debug	12	Out	Debug bus (not required)
scl_in	1	In	I2C Clock In
sda_in	1	In	I2C Data In
sda_out	1	Out	I2C Data Out
sda_oe	1	Out	I2C Data Pad Out Enable (active high)

Start
Stop
rcv_cntr
rcv_reg

sda_in
scl_in
COMP

my_addr
I2C_SM

Cyc_sm

data_out

dat_i

8:1 mux

sda_out

we_o
sel_o
stb_o
cyc_o

ack_i
adr_o

adr_o
dat_o

dat_o

I2C_SLAVE Block Diagram

The “START” detector detects the transition of SDA from high to low while the clock is high.

The “STOP” detector sets when the transition of SDA from low to high occurs while the clock is high.

The “RCV_REG” shifts in the received data when the SCL transitions from low to high. This allows it to capture the data transmitted over the I2C bus.

The “RCV_CNTR” counts the number of bits that have been shifted into “RCV_REG.”

The “COMP” function watches the received data, and when the I2C_SM is in the SM_ADDR state and the data compares to the “my_addr” bus, it indicates an that device has been selected.

The “Data_out” module captures the data from the Wishbone dat_i bus and stores it to be sent out over the I2C SDA_OUT signal through the “8:1 Mux.”

The I2C_SM follows the state diagram below:

IDLE
ADDR

start
cnt8 & !addr_dec |
cnt8 & addr_dec & nack
READ
WRITE

cnt8 & addr_dec & write & ack

cnt8 & addr_dec & !write & ack

start
WAIT

start

cnt8 & nack

stop | reset

I2C SM State Diagram
The state machine goes asynchronously to IDLE when STOP occurs. This is how it exits the READ, WAIT, and WRITE states nominally during burst operations.

The function of the state machine is to interpret multiple I2C sequences, separating them into Address phase which selects the target I2C device followed by either Write or Read phases.

I2C Addr+RW
ack
Wishbone Address

ack

Wishbone
Write Data

ack
Start

Stop

ADDR
WRITE
IDLE
WRITE
IDLE

I2C State Machine Sequence to Write Data to the Wisbhone bus

I2C Addr+RW
ack
Wishbone Address

ack

Start

ADDR
WRITE
IDLE
I2C Addr+RW

ack

Start
ADDR
Wishbone Read Data
ack
Stop

READ

I2C State Machine Sequence to Read Data via the Wishbone bus

The “CYC_SM” is used to cause read and write transactions on the Wishbone bus. The CYC_SM interprets the different points within the I2C sequences and takes appropriate action to move data to or from the I2Cresources across the Wishbone bus.

IDLE
WT0

start
ADDR

ack & target & write
RDATA

ack & target & !write

start
WDATA

ack & write

ack & !write

start
MVDT

clk

clk

start

stop

stop | rst_n

CYC_SM State Machine
Note that ALL of the signal state points mentioned above are synchronized copies of the state signals that exist in the I2C clock domain space. This is necessary to remove any problems with metastability.

I2C Addr+RW
ack
Wishbone Address

ack

Wishbone
Write Data

ack
Start

Stop

IDLE
WT0
ADDR
WDATA
MVDT

CYC_SM state sequence following the I2C Write Transfer

I2C Addr+RW
ack
Wishbone Address

ack

Start

I2C Addr+RW

ack

Start
Wishbone Read Data
ack
Stop

IDLE
WT0
ADDR
RDATA
ADDR
RDATA
IDLE

CYC_SM State sequence following the I2C Read Transfer
The “ADR_O” register captures data upon the state machine moving from ADDR to WDATA. “ADR_O” will increment on succeeding occurrences of ACK while in the WDATA state or RDATA state. This supports burst operations for both read and write sequences.

'The “DAT_O” register captures data upon the state machine moving when the state machine is in the WDATA state and ACK occurs.

Wishbone cycles occur when in the WDATA state and ACK occurs, in the RDATA state and the transfer count = 8, or during the WT0 period to allow pre-fetch of read data.

## EPI_CONTROL_REGS Module
The Epi Control Regs module implements two basic functions. These are the Read/Write path to the programmable I/O pins and the detection of state change on the “received_in” pins. The module is a Wishbone slave and is nominally only accessible from the I2C Slave master.

Signal Name	Width	Direction	Description
rst_n	1	In	Clock
clk	1	In	reset (active low)
addr_o	8	Out	Wishbone Address
dat_i	8	In	Wishbone Data In
dat_o	8	Out	Wishbone Data Out
we_i	1	Out	Wishbone Write
sel_i	1	Out	Wishbone Select (redundant with strobe)
cyc_i	1	Out	Wishbone Cycle
ack_o	1	In	Wishbone Ack
go_ahead	1	Out	Start status_ctl SM – a single clock pulse
cross_point_ctl	48	Out	Cross Point programmable control
relay_out	8	Out	Relay programmable control
oc_out	8	Out	Open Collector programmable Control
stat_in	8	Out	Masked received_in
receive_in	8	In	Received external bus

Write Addressable registers
Address	Reg Name	Description
8'h40	MASK	Masks the received_in bus when bit is 0.
8'h41	RELAY	Controls “relay_out[7:0]”
8'h42	OC_OUT	Controls “oc_out[7:0]”
8'h43	CP0	Controls “cross_point_out[7:0]”
8'h44	CP1	Controls “cross_point_out[15:8]”
8'h45	CP2	Controls “cross_point_out[23:16]”
8'h46	CP3	Controls “cross_point_out[31:24]”
8'h47	CP4	Controls “cross_point_out[39:32]”
8'h48	CP5	Controls “cross_point_out[47:40]”

Note all read accesses receive the STAT_IN bus which is a time delayed version of the XOR output.

Addr
Dec

addr_i
sel_i
cyc_i
we_i
rcv_mask
mask
relay
oc_out
cp0
cp5

XOR
last_rcv_in
AND

receive_in

go_ahead

stat_in

stat_in

receive_in
dat_i

relay_out

oc_out

cross_point_out
dat_o

ack_o

EPI_CTL_REGS block diagram
There are 9 separate registers that can be written too, while a read to any address returns the “STAT_IN” bus.
The “receive_in” bus is ANDed with the value in the “MASK” register and delayed by one clock. The result of the masked value is compared to the delayed value to detect a change in state. Any change in state will cause the “go_ahead” pulse to occur.

## STATUS_MCODE
This module implements a byte addressable 16X8 memory array that is attached as a Wishbone slave to the internal Wishbone bus. Bank 0 receives even addresses, while Bank1 receives odd addreses. A second read port feeds the Microcode word over to the “STATUS_CTL” module.

Signal Name	Width	Direction	Description
rst_n	1	In	Clock
clk	1	In	reset (active low)
addr_i	8	Out	Wishbone Address
dat_i	8	In	Wishbone Data In
dat_o	8	Out	Wishbone Data Out
we_i	1	Out	Wishbone Write
sel_i	1	Out	Wishbone Select (redundant with strobe)
cyc_i	1	Out	Wishbone Cycle
ack_o	1	In	Wishbone Ack
mc_addr	3	In	Microcode Address
mc_word	16	Out	Microcode Data Word

Read/Write address descripton
Address	Reg Name	Description
8'h00	Bank0 byte 0	Microcode Word 0 – lower byte
8'h01	Bank1 byte 0	Microcode Word 0 – upper byte
8'h02	Bank0 byte 1	Microcode Word 1 – lower byte
8'h03	Bank1 byte 1	Microcode Word 1 – upper byte
8'h04	Bank0 byte 2	Microcode Word 2 – lower byte
8'h05	Bank1 byte 2	Microcode Word 2 – upper byte
8'h06	Bank0 byte 3	Microcode Word 3 – lower byte
8'h07	Bank1 byte 3	Microcode Word 3 – upper byte
8'h08	Bank0 byte 4	Microcode Word 4 – lower byte
8'h09	Bank1 byte 4	Microcode Word 4 – upper byte
8'h0A	Bank0 byte 5	Microcode Word 5 – lower byte
8'h0B	Bank1 byte 5	Microcode Word 5 – upper byte
8'h0C	Bank0 byte 6	Microcode Word 6 – lower byte
8'h0D	Bank1 byte 6	Microcode Word 6 – upper byte
8'h0E	Bank0 byte 7	Microcode Word 7 – lower byte
8'h0F	Bank1 byte 7	Microcode Word 7 – upper byte

BANK0
BANK1

addr_i[0]
1
0

dat_o
mc_word[7:0]
mc_word[15:8]

addr_i[0]

!addr_i[0]

addr_i[3:1]
dat_i[7:0]
sel_i
cyc_i
we_i
ACK

sel_i
cyc_i

ack_o

mc_addr[2:0]

mc_addr[2:0]

STATUS Microcode store block diagram

The Wishbone bus organizes the memory into two banks, each 8 bits wide that take on even an odd addresses respectively on the Wishbone bus. The second read path is addressed by mc_addr[2:0] and supplies the “mc_word” bus.

## STATUS_CTL
The “STATUS_CTL” module is serves as a Wishbone master which causes I2C messages to be sent via the I2C Master module. The “STATUS_CTL” receives it's micro-coded instructions from the “STATUS_MCODE” module via the “mc_word” bus and interprets them as to the action it's to take.

Signal Name	Width	Direction	Description
rst_n	1	In	Clock
clk	1	In	reset (active low)
addr_o	8	Out	Wishbone Address
dat_i	8	In	Wishbone Data In
dat_o	8	Out	Wishbone Data Out
we_o	1	Out	Wishbone Write
sel_o	1	Out	Wishbone Select (redundant with strobe)
cyc_o	1	Out	Wishbone Cycle
ack_i	1	In	Wishbone Ack
mc_addr	3	Out	Microcode Address
mc_word	16	In	Microcode Data Word
go_ahead	1	In	Start interpreting the Microcode
stat_in	8	In	Synchronized version of masked “received_in” bus

The module receives “mc_word” which controls the operation of the module. The table below defines how the state machine decodes the micro-control word.

Signal Name	Function
mc_word[7:0]	Data Out/Comparison word
mc_word[10:8]	Address to I2C Master
mc_word[11]	Source Select 0 = mc_word[7:0] 1=status_in
mc_word[14:13]	00 – Wishbone Write Operation / 01 – Wishbone Read and Compare/Loop / 10 = Wait till Interrupt / 11 – Undefined
mc_word[15]	Stop execution after transaction

This section provides a block diagram of the STAT_CTL module:

Stat_SM

mc_word[15:8]
mc_addr
clr_mcadr

incr_mcadr

mc_addr
Wishbone
Gen

run_cyc

cyc_o
stb_o

we_o

ack_i

mc_word[7:0]

stat_in

dat_o
AND

neq

STAT_CTL Block Diagram

IDLE
RUN0
!ack
loop & neq &
!we0
stop
RUN1

WAIT

int

       Y/
run_cyc
Y
Y
N
N
N
Y
N
go_ahead/
run_cyc
wait_till_int
!wait_till_int/
run_cyc
/run_cyc
/clr_mcadr
/incr_mcadr
/run_cyc

STAT_CTL State Machine

## WB_ARB_MUX
This module provides arbitration services and muxes the address bus and data_out buses.